Everex Micro Enhancer.

  Ev678 and Ev236 use Trident chips.



  3C2h (r/W)): Misc Output Register
    bit 5  Bit 1 of Bank No.

  3C4h index  8  (R/W):
    bit 7  Bit 0 of Bank no.


  Bank switching.

  Everex uses a two bit bank no. with bit 0 in 3C4h index 8 bit 7
  and bit 1 in 3C2h bit 5.



  ID Everex Micro Enhancer:

  RP.AX=$7000;
  RP.BX:=0;
  INTR($10,RP):
  IF RP.AL=$70 THEN
  BEGIN
    NR:=RP.DX SHR 4;
    IF (NR=$678) or (nr=$236) then TRIDENT
    else EVEREX Ev(Nr).
  END;


  BIOS extensions:

----------100070-----------------------------
INT 10 - VIDEO - Everex Micro Enhancer EGA/Viewpoint VGA - EXTENDED MODE SET
        AX = 0070h
        BL = mode (see below)
SeeAlso: AH=00h,AX=6F05h,AX=7000h/BX=0004h,AH=FFh"GO32"

Values for video mode:
     text/ text   pixel pixel    colors disp scrn monitor  adapter
     grph  resol  box   resoltn         page addr
 00h = G                640x480   16              multsync EGA,VGA
 01h = G                752x410   16              multsync EGA,VGA
 02h = G                800x600   16              multsync EGA,VGA
 03h = T   80x34                                  multsync EGA,VGA
 04h = T   80x60                                  multsync EGA,VGA
 05h = T   94x29                                  multsync EGA only
 06h = T   94x51                                  multsync EGA only
 07h = T  100x43  8x14            16                       VGA only
 08h = T  100x75  8x8             16                       VGA only
 09h = T   80x44                                  EGA      EGA only
 0Ah = T  132x25                                  EGA      EGA,VGA
 0Bh = T  132x44                                  EGA      EGA,VGA
 0Ch = T  132x25                                  CGA      EGA only
 0Dh = T   80x44                                  mono     EGA only
 0Eh = T  132x25                                  mono
 0Fh = T  132x44                                  mono
 10h =	 reserved
 11h = G                1280x350  4               EGA only
 12h = G                1280x600  4               EGA only
 13h = G                640x350   256             EGA only
 14h = G                640x400   256
 15h = G                512x480   256
 16h = T   80x30  8x16            256             VGA only
 18h = T  100x27  8x16            16              VGA only
 20h = G                1024x768  16              Everex 629,678
 21h = T  160x64  8x16  1280x1024 16              1MB VGA only
 30h = G                640x480   256             Everex 629,678
 31h = G                800x600   256             Everex 629,678
 32h = G  128x48  8x16  1024x768  256             1MB VGA only
 40h = T  132x30  8x16            16              VGA only
 50h = T  132x32  8x16            mono            VGA only
 62h = G   40x25  8x8   320x200   32K             Vwpt TC (EV629)
 70h = G   64x30  8x16  512x480   32K             Viewpoint TC
 71h = G   80x30  8x16  640x480   32K             Viewpoint TC
 76h = G   64x30  8x16  512x480   16M             Viewpoint TC
 77h = G   80x30  8x16  640x480   16M             Viewpoint TC
----------107000BX0000-----------------------
INT 10 - Everex Extended Video BIOS - RETURN EMULATION STATUS
        AX = 7000h
        BX = 0000h
Return: CL = monitor type
             00h mono
             01h CGA
             02h EGA
             03h digital multifrequency
             04h IBM PS/2 
             05h IBM 8514
             06h SuperVGA
             07h analog multifrequency
             08h super multifrequency
        CH = feature bits
             bits 7,6: 00 = 256K memory
                       01 = 512K memory
                       10 = 1024K
                       11 = 2048K memory
             bit 5:    special oscillator present
             bit 4:    VGA protect enabled
             bit 0:    6845 emulation
        DX = video board info
             bits 4-15: board ID model
             bits 0-3:  board ID revision
        DI = BCD BIOS version number
----------107000BX0004-----------------------
INT 10 - Everex Extended Video BIOS - GET PAGING FUNCTION POINTER FOR CURR MODE
        AX = 7000h
        BX = 0004h
Return: ES:DI -> FAR paging function (call with DL = page to set)
Note:   the word preceding ES:DI is the length of the function in bytes, and
        the last byte of the function is a FAR return instruction.
SeeAlso: AX=4F05h,AX=7000h/BX=0000h,AX=7000h/BX=0005h
----------107000BX0005-----------------------
INT 10 - Everex Extended Video BIOS - GET SUPPORTED MODE INFO
        AX = 7000h
        BX = 0005h
        CL = maximum number of modes to get info for
        CH = mode type to get info for (see below)
        DL = monitor type to get info for
        ES:DI -> buffer for mode info (see below)
Return: CL = total number of modes fitting criteria
        CH = size of each info record
SeeAlso: AX=7000h/BX=0000h,AX=7000h/BX=0004h

Values for mode type:
 00h all modes
 01h monochrome text modes
 02h color text modes
 03h four-color CGA graphics modes
 04h two-color CGA graphics modes
 05h 16-color graphics modes
 06h 256-color graphics modes

Format of mode information record:
Offset Size  Description
 00h   BYTE  mode number (bit 7 set if extended mode)
 01h   BYTE  mode type (see above)
 02h   BYTE  info bits
             bits 7,6 reserved
                    5 monochrome mode
                    4 interlaced display
                    3 requires special oscillator
                  2,1 memory required 
                      00 = 256K
                      01 = 512K
                      10 = 1024K 
                      11 = 2048K
                    0 reserved
 03h   BYTE  font height
 04h   BYTE  text columns on screen
 05h   BYTE  text rows on screen
 06h   WORD  number of scan lines
 08h   BYTE  color information
             bits 7-4 reserved
                  3-0 bits per pixel