VME KERMIT User Guide
                             =====================
 
 
 
 
 
     This  document  describes  how to use the VME implementation of KERMIT
     produced at the South West Universities Regional Computer Centre.
 
     The information in this edition applies to version 1.01 of VME KERMIT.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                                               EDITION 1.01
                                                               October 1986
 
 
 
                              ACKNOWLEDGEMENT
 
    The layout and content of this document is derived from the  'USER GUIDE
    FOR BBC KERMIT'  written by Alan Phillips of the Computing Department at
    the University of Lancaster. We are grateful for his permission  to  use
    this material.
 
 
 
 
 
 
 
 
 
 
 
                             VME KERMIT User Guide
 
                                    CONTENTS
 
               1.  INTRODUCTION
 
               2.  AN OVERVIEW OF KERMIT
 
               3.  CONTROLLING VME KERMIT
                   3.1  Entering VME KERMIT
                        3.1.1 The OPTION parameter
                        3.1.2 The VME_FILE parameter
                        3.1.3 The REM_FILE parameter
                   3.2  Leaving VME KERMIT
                   3.3  VME KERMIT command language
                        3.1.1  Command format
                        3.3.2  Abbreviating commands
                        3.3.3  Numeric parameters
                        3.3.4  The help facility
 
               4.  TRANSFERRING FILES WITH KERMIT
                   4.1  Principles
                   4.2  Setting file type
                        4.2.1  How files are organised
                        4.2.2  Sending eight-bit data
                        4.2.3  Binary files
                        4.2.4  ASCII files
                        4.2.5  EBCDIC files
                   4.3  File transfer as a server
                   4.4  File transfer as a non-server
                        4.4.1  Sending files as a non-server
                        4.4.2  Receiving files as a non-server
                   4.5  Handling problems
                   4.6  Advanced facilities
                        4.6.1  Incomplete file transfers
                        4.6.2  Using timeouts
                        4.6.3  Protocol control
 
               5.  COMMANDS FOR GENERAL CONTROL OF KERMIT
 
               6.  COMMANDS FOR TRANSFERRING DATA
 
               7.  COMMANDS FOR PROTOCOL CONTROL
 
               8. OBTAINING, BUILDING AND MODIFYING VME KERMIT
                   8.1 Obtaining VME KERMIT
                       8.1.1 The source files
                   8.2 Building VME KERMIT from source
                   8.3 Changing KERMIT defaults
 
               Appendix 1. VME KERMIT capabilities
 
               Appendix 2. Valid VME control characters
 
               Appendix 3. Running KERMIT over a JNT PAD
 
 
 
 
 
 
 
                             VME KERMIT User Guide
 
 
 
     1: INTRODUCTION
     ===============
 
        This user guide describes the VME implementation of KERMIT produced
     by  the  South  West  Universities  Regional  Computer  Centre at Bath
     University. It is intended to provide enough information for a  novice
     KERMIT  user  to  be  able to transfer data to and from VME to another
     KERMIT system. Other KERMIT systems are desribed only in passing: thus
     a user would almost certainly need  to  consult  the  equivalent  user
     guide for the KERMIT system on the other machine.
 
        The guide is divided into several chapters. The first chapter is  a
     general  overview of KERMIT as a whole, and explains its advantages as
     a file transfer system over "dumb capture" pograms. The  next  chapter
     describes  the  command  language that VME KERMIT uses. Following that
     are chapters that describe how to use VME KERMIT to transfer data.
 
        The  final chapters comprise the "reference section". They describe
     in full detail the commands available in VME KERMIT, grouping them  by
     functionality (i.e. "Commands for file transfer", etc).
 
        The very last chapter of the guide  describes  how  to  obtain  VME
     KERMIT,  and, having obtained it, how to build it from the S3 language
     source.
 
 
 
        VME KERMIT is, of course, freely available to anyone who wants  it.
     It  can  be  obtained  from Lancaster University's KERMIT distribution
     service over file transfer from their VAX 11/780 system. The Lancaster
     distribution  service  also  maintains  on-line  bulletin files giving
     details  new releases of VME KERMIT and of reported bugs: these can be
     consulted in a public-access username.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      1-1
                             VME KERMIT User Guide
 
 
 
     2: AN OVERVIEW OF KERMIT
     ========================
 
        KERMIT is a system, devised at the Center for Computing  Activities
     at  the University of Columbia, New York (CUCCA), to permit the simple
     and flexible transfer of data from a microcomputer to a  mainframe  or
     another  microcomputer. CUCCA retain the copyright on KERMIT, but have
     published full information on it and permit anyone to implement it  on
     their own machines, provided this is not done for commercial purposes.
     The  result  is  that  KERMIT is now available on a very wide range of
     machines indeed: very few micros and mainframes  now  do  not  have  a
     KERMIT of some sort available for them.
 
        The  primary  design aim of KERMIT is to permit the transfer of any
     data whatsoever between systems, and to make the data  usable  on  the
     system that receives it if this is possible. To illustrate why this is
     important,  and  not  possible with simple systems, we can consider an
     ordinary terminal emulation system that allows  data  to  be  captured
     into files or sent from them.
 
        Simple  terminal  emulator  systems,  such  as  those  commercially
     available  for  many  micros,  do  permit you to transfer files from a
     mainframe in a rudimentary way. You would tell the  emulator  to  copy
     any  characters  that  appear  on the screen into a file, then ask the
     mainframe to display the file. The reverse process would let you input
     data into a mainframe file from your micro's discs.
 
        The  problems arise in the nature of the communications system that
     connect the micro to the mainframe, and how the mainframe itself  uses
     this  system.  A  character of data in a file occupies one byte, which
     consists of 8 binary digits or "bits". If you regard  the  pattern  of
     bits representing a character as a number, this allows numbers ranging
     from  0  to  255 to be used. However, many communications systems will
     allow only 7 of the eight bits to be transmitted along them. The  most
     significant   bit,   termed   the   "parity   bit",  is  used  by  the
     communications system as an error-checking device. Thus,  even  though
     you  send  a byte of 8 bits to the mainframe, it may receive only 7 of
     them. This immediately restricts the range of characters that  can  be
     sent to those whose codes are in the range 0 to 127.
 
        A  further  restriction may be imposed if the communications system
     uses some of those characters  for  its  own  control  purposes:  thus
     systems  often  will  use  the characters whose codes are 17 and 19 to
     prevent overloads occurring. In  such  systems,  you  cannot  transmit
     these  characters  at  all.  To make matters even worse, some machines
     will (apparently arbitrarily) decide that you could not possibly  want
     to  send some characters, so, if you do send them, it will change them
     into something else entirely.
 
        The  character  range 0 to 127 covers all the printable characters,
     so that transferring text files should  just  about  be  possible.  Of
     course,  if  the  communications  line  you are using is unreliable or
     noisy (a slow dial up line, for instance) there is nothing to  prevent
     data  being  garbled  in  transmission, so that you will never be sure
     sure that the data that arrives is the data that you sent.
 
 
                                      2-1
                             VME KERMIT User Guide
 
 
        KERMIT overcomes all these difficulties by  encoding  the  data  it
     sends  according  to  a  standard  set  of rules or "protocol". KERMIT
     recognises  that  many  characters  cannot  be  transmitted   down   a
     communications  line,  so  if  those  characters  occur,  they will be
     translated into something that will be transmitted. The receiving end,
     of course, will translate them back again  to  what  they  were.  This
     technique  enables  you  to  send  any  data at all, even machine code
     programs. It further guarantees that the data you  send  is  the  data
     that  arrives,  since  KERMIT  uses  special  methods  for   detecting
     garbling  and  will  repeat any transmissions that did not get through
     correctly.  KERMIT's  encoding  and  checking  techniques   are   more
     efficient than some other systems that offer this facility, since only
     bytes that need encoding actually are encoded, thus keeping the volume
     of data sent to the minimum possible.
 
 
        Besides  the problems of actually transferring data corectly, there
     is  the  problem  of  making  it  usable  on  the  other  end  of  the
     transmission link. If you are sending, say, a SAVEd BASIC program from
     a micro to VME, this isn't a problem, since VME can't understand micro
     BASIC anyway. Nor does it matter if you use the VME system only as  an
     archive:  it's irrelevant how the data is held on VME, as long as when
     it is brought back to the micro side it looks the same as when it  was
     sent.
 
        The  usability  problem  does appear, though, if you want to move a
     file from a micro to VME and then actually use it on VME.  You  might,
     for  instance, word process a file on the micro then send it to VME to
     be printed. In this case,  you  do  NOT  want  to  transfer  the  data
     byte-for-byte,  since  the  way  the  micro and VME denote things like
     the end of each line of text will almost certainly be different.  What
     you require is that the file of printable lines on the micro which you
     can process on that machine, becomes a file of  printable  records  on
     VME, that can be processed there.
 
        Using  a  dumb terminal emulator system would probably let you send
     the data, but it would appear byte-for-byte as it was  on  the  micro.
     And probably you would get a  file  on  VME  with extra line-feeds and
     carriage-returns that would need laborious editing  before  you  could
     use the file sensibly.
 
        With  KERMIT  the  problem  can  easily be circumvented. The KERMIT
     protocols define a standard way of indicating the end of  a  printable
     line.  When  you  send  a  file  from  VME,  VME KERMIT will translate
     whatever ends the lines of text in your file into this  standard  form
     before  sending  the  data.  The  receiving  end, seeing this standard
     end-of-line indicator, will translate it  into  however  IT  indicates
     end-of-line.  You  thus  end  up  with a usable file of lines, with no
     extra characters anywhere.
 
 
 
 
 
 
 
 
 
                                      2-2
                             VME KERMIT User Guide
 
 
        The requirements you must meet before using KERMIT are simple.  You
     will  need a KERMIT in your micro which supports terminal emulation; a
     KERMIT program in the VME system you wish to transfer data to;  and  a
     way  of  linking  the machines, be it a network, an ordinary cable, or
     whatever.
 
        Micro to mainframe transfers involves entering the micro's terminal
     emulator  program:  you  initially use this to log in to VME as though
     the micro was an ordinary terminal. Once logged in, you start the  VME
     KERMIT program, and can then flip from giving commands to VME  KERMIT,
     to  giving  commands to the micro KERMIT. You tell one machine that it
     is going to receive a file, tell the other to send it,  and  sit  back
     and relax while it happens.
 
        Some micro KERMIT's provide one further facility to help you  spend
     time  doing  more useful things. As well as sending one file at a time
     from one machine to the other, you can send them in groups: thus,  you
     could  say  "send  all  the  files  on my disc to VME" in one command.
     The KERMIT programs will send the files one by one until all are gone,
     quite automatically. This facility is not available with VME KERMIT.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      2-3
                             VME KERMIT User Guide
 
 
 
     3: CONTROLLING VME KERMIT
     =========================
 
        In this section we shall look at how you start and stop VME KERMIT,
     and also how its command language operates.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      3-1
                             VME KERMIT User Guide
 
 
 
     3.1 ENTERING VME KERMIT
     -----------------------
 
        To  invoke VME KERMIT you must log in to VME and issue the command:
 
                 KERMIT ( OPTION   = @ initial mode         @ ,
                          VME_FILE = @ name of VME file     @ ,
                          REM_FILE = @ name of remote file  @ ,
                          RESPONSE = @ result code variable @ )
 
        to the VME command prompt.
 
 
      3.1.1. The OPTION Parameter
 
            This parameter defines which mode VME KERMIT is to start up in.
            If  you  set  this  parameter to COMMAND (the default) then VME
            KERMIT will start up in command mode and you will  be  prompted
            to  type comands. You must not specify the VME_FILE or REM_FILE
            parameters when you have set the OPTION parameter to COMMAND.
            If  you wish to initiate a file transfer directly you may do so
            by setting the OPTION parameter to either RECEIVE  (VME  KERMIT
            is  to  receive a file) or SEND (VME KERMIT is to send a file).
            For RECEIVE, the VME_FILE parameter is optional  but  you  must
            not  set  the  REM_FILE  parameter.  For  SEND,  the  VME_FILE
            parameter is mandatory and it must be set to the  name  of  the
            VME  file  to  be  sent.  The  REM_FILE  parameter  however  is
            optional.
            Alternatively you may wish to enter server  mode  directly, you
            may  do  this by setting the OPTION parameter to SERVER. As for
            COMMAND mode the VME_FILE and REM_FILE parameters must  not  be
            specified.
 
 
      3.1.2. The VME_FILE parameter
 
            This parameter specifies the name of the VME file to be used in
            the file transfer.
            If you have set the OPTION parameter to COMMAND or  SERVER  you
            must not set this parameter.
            This  parameter  is optional if you set the OPTION parameter to
            RECEIVE. If it is given then it must contain the  name  of  the
            VME  file  to  receive  the data. If you default this parameter
            then  KERMIT  will  take  the  VME  file  name  from  the  file
            indentified by the micro KERMIT.
            This parameter is manadatory when you set the OPTION  parameter
            to  SEND  and  it  must  contain the name of the VME file to be
            transfered.
 
 
      3.1.3. The REM_FILE parameter
 
            This  parameter  specifies  the  file name that VME KERMIT will
            send to the micro KERMIT to identify the file.
            This parameter is optional when the OPTION parameter is set  to
            SEND, but  must  be  omitted in all other cases. If you set the
 
                                      3-2
                             VME KERMIT User Guide
 
            option parameter to SEND and default  this  parameter  the  VME
            KERMIT will send to the micro KERMIT a file name taken from the
            VME file name.
 
 
     3.1.4. The RESPONSE parameter
 
            This parameter is used to return result codes. VME KERMIT  does
            not  generate  any  result  codes  of it's own but standard VME
            result codes may be returned. Normally this parameter should be
            omitted.
 
 
 
     3.2 LEAVING VME KERMIT
     ----------------------
 
        To  leave  VME KERMIT you would normally use the EXIT command. This
     will close down KERMIT and return to the VME command level.
 
        Alternatively, if you are running VME KERMIT in server mode you can
     close  KERMIT  remotely  and either return to the VME command level or
     log out the VME terminal session.
 
 
 
     3.3 VME KERMIT COMMAND LANGUAGE
     -------------------------------
 
        You  control  what  you want VME KERMIT to do, and how it should do
     it, by giving it commands in its "command language". The format of the
     command language closely  follows  that  used  on  most  other  KERMIT
     implementations on other machines.
 
 
     3.3.1. Command format
 
           When you enter VME KERMIT, you will see a prompt on the screen
 
                                  VME Kermit>
 
          This indicates  that  KERMIT  is expecting you to type a command.
          KERMIT commands can be typed in upper case, lower  case,  or  any
          mixture of the two as you please.
 
           KERMIT  commands  take the form of a command name, such as "SET"
          sometimes followed by one or more further pieces  of  information
          or  "parameters",  which  must  be  separated  from each other by
          spaces.
          For example, one command you might use is
 
                                  SET RETRY 10
 
          to  set  the  number  of  times an attempt will be made to send a
          particular packet before giving up. Here the  command  is  "SET",
          and  RETRY  and 10 are the parameters to the command. Since there
          are a large number of variations to the SET  command,  these  are
          often  referred  to  in  this guide as separate comands. Thus you
 
                                      3-3
                             VME KERMIT User Guide
 
          see references  to  the  "SET  FILE  TYPE  BINARY"  command,  for
          instance.  You can regard this as either a command whose name has
          spaces in it, or as a form of the  SET  command  with  parameters
          FILE,  TYPE  and  BINARY.  In either case, the effect will be the
          same.
 
           At the end of each command you should press the  RETURN  key  to
          send  the  line  to  KERMIT for action. If you have made a typing
          mistake you can use the delete key and cancel key exactly as  for
          other VME commands.
 
           The  reference  section  at  the  end  of  this  guide gives the
          complete specification  of  all  the  VME  KERMIT  commands.  The
          commands  are  grouped according to their function (such as "file
          transfer control"), rather than in one  alphabetical  list.  Thus
          you  will  find  variations  of the SET command appearing in many
          places, grouped with other commands that  function  in  the  same
          area.
 
           The  reference  section presents each command in a formal way to
          show you exactly what you are allowed to type at any  point.  You
          might find one command described as having a format
 
                               SET PAUSE <number>
 
          for example. Here the fixed parts, that you would always include,
          are  shown in capitals. The third part of the command, "<number>"
          is enclosed in "<>" brackets to show that here you  must  provide
          your  own  parameter  value.  The  fact  that  it  says  "number"
          indicates that what you should type is a number of some sort: the
          description of the command will tell you what sort of number  you
          must  provide and why. Note that you don't type the "<>" brackets
          yourself here. Thus, a valid way of using this command might be
 
                                  SET PAUSE 10
 
          where you have supplied the  numeric  value  "10"  where  it  was
          expected.
 
           Sometimes,  not  all  the  parameters  of  some commands need be
          typed. In these cases, VME KERMIT will take a "default" value for
          the parameter you did not supply. The reference section will tell
          you which parameters can be omitted, and what values  VME  KERMIT
          will assume if they are omitted.
 
 
     3.3.2. Abbreviating commands
 
           To  reduce  the amount of typing that you need to do, VME KERMIT
          allows you to abbreviate all commands and  most  parameters.  You
          may  abbreviate  to  as few characters as you wish, provided that
          what you type is unique. Thus
 
                                   HELP
                                   HEL
                                   HE
                                   H
 
 
                                      3-4
                             VME KERMIT User Guide
 
          are legal, but
                                   S
 
          is not, since it could stand for either SEND, SERVER, SET,  SHOW
          or STATISTICS. To take a full example, you could type either
 
                             SET FILE TYPE BINARY
 
          or abbreviate it as far as
 
                                   SET F T B
 
 
     3.3.3. Numeric parameters
 
           Except  where explicitely stated, numeric parameters to commands
          can be typed in either decimal or hexadecimal.  By  default,  VME
          KERMIT  expects  the  value to be decimal, but you can indicate a
          hexadecimal number by preceding the parameter with an "X".
 
           Thus
 
                                      123
 
          is a decimal value, and
 
                                      X123
 
          is a hexadecimal value.
 
 
 
     3.3.4. The help facility
 
           Quite  often,  you  may wish a reminder as to what parameters or
          commands you can give. KERMIT has a "help" facility that will act
          as an "aide-memoire" for you.
 
           To use help, simply type HELP in response to the command prompt.
          KERMIT will immediately give you a list of the commands available
          and  the  option  of  requesting  further  information  about the
          commands.
 
          For example, if you type HELP after the prompt thus:
 
               VME Kermit> HELP
 
          KERMIT  will  output  a list of the commands you can use. You may
          then request more information about one of the commands from  the
          menu.
 
           The  HELP  command  may  be  augmented  by  folowing  it  by  a
          command name and parameters.
 
 
 
 
 
 
                                      3-5
                             VME KERMIT User Guide
 
          For  example,  if  you  require  help  for  the "SET" command you
          type
 
                           VME Kermit> HELP SET
 
          VME KERMIT will then give you an explanation ot the "SET" command
          and  a  list  of the parameters available. You will then be given
          the option of requesting further information about the parameters
          and their values.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      3-6
                             VME KERMIT User Guide
 
 
 
     4: TRANSFERRING FILES WITH KERMIT
     =================================
 
        The primary use of VME KERMIT is to transfer files between it and a
     microcomputer.  The  methods  used  will  be  substanstially  the same
     whatever the other system is, since any KERMIT system should  be  able
     to  communicate  with any other. Though the general techniques will be
     same, the exact commands used to control the  different  KERMITs  will
     vary  from  one  system  to another. You will need to consult the user
     guides of the other system to discover how it should be controlled. In
     this section we shall cover in detail how VME KERMIT is controlled.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      4-1
                             VME KERMIT User Guide
 
 
     4.1 PRINCIPLES
     --------------
 
        KERMIT differs from other "dumb" file transfer systems (such as you
     might  find  in a terminal emulator ROM, for instance) in that it aims
     to transfer files in a USABLE way between systems. Thus, if you have a
     program  source  on  your  micro's  discs  that you can edit with some
     editor, and transfer this to VME, the resulting file  should  also  be
     editable  using VME's editors. KERMIT will resolve all the differences
     in how files are stored on your behalf, so that, in this example,  the
     VME  file  will not contain extra line-feed characters at inconvenient
     places that the VME editor cannot handle.
 
        Transferring  files with KERMIT involves several discrete steps. We
     shall consider here the most common case of transfer  to  and  from  a
     microcomputer.
 
          1. The micro KERMIT is entered and set up  for  the  transfer. In
          particular, you may wish to tell KERMIT what types of file are to
          be moved. You will also need to set the parameters  for  terminal
          emulation,  and,  depending  on the micro system's needs, you may
          need to change some of the  more  detailed  aspects  of  the  VME
          KERMIT's operation.
 
          2. Terminal emulation mode is entered, and the micro is logged in
          to VME as though it were an ordinary terminal.
 
          3. Operating as a terminal, the VME KERMIT program is started.
 
          4. Commands  can  then  be given to the VME KERMIT (from terminal
          emulation mode) and to the micro's KERMIT  (from  KERMIT  command
          mode).  The  two  KERMIT systems will communicate with each other
          using the standard KERMIT protocol.
 
          5. After the transfers are done, the terminal is logged out  from
          the VME system.
 
     In  practice,  the  steps  taken  will  range up and down this list as
     required. For example, VME KERMIT parameters can  be  changed  at  any
     time,  not  only  at  the start, and if you are moving several tyes of
     file you will need to change them frequently. In the sections below we
     shall consider the various actions you will need to take; the order of
     doing them is up to you.
 
 
 
     4.2 SETTING FILE TYPE
     ---------------------
 
 
     4.2.1 How files are organised
 
          VME  KERMIT can only operate on serial access files, and the user
          must have the required access  permissions  (read  or  write,  as
          necessary). The maximum record size that VME KERMIT can handle is
          4096 bytes.
 
 
                                      4-2
                             VME KERMIT User Guide
 
     4.2.2 Sending eight bit data
 
           Futher more VME KERMIT restricts data it sends to only 7 bits in
          each byte: thus you can only normally send characters whose ASCII
          codes  are in the range 0 to 127. However, every binary file will
          contain bytes from the whole character set, with codes from 0  to
          255.
 
           KERMIT   in   general   has  a  technique  for  overcoming  this
          restriction, by encoding characters  in  the  range  128  to  255
          into  special  sequences  that can be sent down any communication
          line. VME KERMIT and most modern KERMITs will use this technique,
          which  is  known  as "eigth-bit-prefixing", but you may encounter
          an older implementation on some machine that does not support it.
          In  this case it will not be possible to transfer the file. There
          is regrettably, no way round this problem from within KERMIT.
 
     4.2.3. Binary files
 
          These  files  contain  data that is not primarily printable text,
          such as machine-code programs. When you transfer these files, you
          wish  every byte in the file on one system to appear unchanged in
          the file on the other system, regardless of what it is.
 
          You tell KERMIT that you  are  handling  binary  files  with  the
          command
 
                              SET FILE TYPE BINARY
 
          which  tells  it  not  to change any data that it either sends or
          receives. Note here that you  may  need  to  issue  a  comparable
          command  to  the micro KERMIT, to prevent it trying to manipulate
          the data.
 
     4.2.4. ASCII files
 
          These  files  contain  data that is primarily printable text, but
          they also contain some characters whose codes are in the range  0
          to 255, such as word processing text files. As with binary files,
          the data is transferred  byte-for-byte,  but  in  this  case  the
          record format is maintained.
 
          You  tell  KERMIT  that  you  are  handling  ASCII files with the
          command
 
                              SET FILE TYPE ASCII
 
          which  tells  it  not  to change any data that it either sends or
          receives, but it is to recognise end of record delimeters.
 
     4.2.5. EBCDIC files
 
          These  files  contain  printable  text, such as program listings.
          When you transfer one of these files, you do not necessarily want
          a  byte-for-byte  transfer,  since the two machines may differ in
          how they store text files.  VME  for  example,  uses  the  EBCDIC
          character code to store text files,  whilst  most micro's use the
          ASCII character code. The KERMIT standards defines a fixed way in
 
                                      4-3
                             VME KERMIT User Guide
 
          which things such as end-of-line are transferred: VME KERMIT will
          translate your data to this standard format, and  the  other  end
          will  then  translate  the  standard format into whatever its own
          specific requirements are.
 
          You tell VME KERMIT that EBCDIC text files are to be  transferred
          with the
 
                              SET FILE TYPE EBCDIC
 
 
 
     4.3 FILE TRANSFER AS A SERVER
     -----------------------------
 
        VME  KERMIT  will  run as a KERMIT server, but it is essential that
     your micro KERMIT is able to communicate with a server:  that  is,  it
     must support the commands GET and BYE or FINISH.
 
      You should put VME KERMIT into server mode with the command "SERVER".
     You should then use your micro KERMITs local escape sequence to return
     to  command  mode. The operation of both KERMITs can now be controlled
     from your micro KERMIT, and your micro KERMITs user guide should  give
     you further information regarding running with a server.
 
 
 
     4.4 FILE TRANSFER AS A NON-SERVER
     ---------------------------------
 
        Transferring  data  as  a  non-server is a little more complicated,
     since you will need to continually  change  from  the  micro  KERMITs
     command mode to terminal mode and back again. With a little  practice,
     though, the technique becomes natural.
 
     4.4.1. Sending files as a non-server
 
          To send a file as a non-server you use the command SEND. However,
          you must also tell the micro KERMIT that a file is on its way.
 
          One means of doing this is as follows:
 
               a. In terminal mode, start the VME KERMIT program, and issue
               the  SEND command. This tells it to send a file to the micro
               system. Normally, VME KERMIT will pause for  30  seconds  to
               enable  you  to escape back and issue commands to your micro
               KERMIT.
 
               b. Use  your  micro  KERMITs local escape sequence to return
               back to its command mode.
 
               c. Issue  the  micro  KERMIT  RECEIVE  command. When the VME
               KERMITs delay expires, it will start to send the file.
 
     4.4.2. Receiving files as a non-server
 
          If  the  VME  KERMIT system is not running as a server, you will
          need to transfer files from it by the exact reverse of the above
 
                                      4-4
                             VME KERMIT User Guide
 
          SEND procedure:  all  you  need to do is reverse the roles of the
          two machines. Thus, you could take the following steps:
 
               a. In terminal mode, start the VME KERMIT program, and issue
               its RECEIVE command. This tells it that a file is on its way
               from the micro system.
 
               b. Use  your  micro KERMITs local escape sequence to return
               back to its command mode.
 
               c. Issue   the  micro  KERMITs  SEND  command.  There  will
               normally be a delay before anything happens.  The  interval
               may  be anything from a few seconds upwards. When the micro
               system's delay time expires, it will start to send the file
 
 
 
     4.5 HANDLING PROBLEMS
     ---------------------
 
        By  design,  KERMIT  is a highly reliable file transfer system, and
     performs considerably better than any "dumb capture" facility within a
     terminal emulator. The error-detection capabilities of  KERMIT  ensure
     that  data  is  transmitted  correctly:  in  the  rare cases where the
     communications system you are using is unreliable, KERMIT systems will
     abort a file transfer rather than transfer garbage.
 
        That said, there are some cases where you  may  need  to  give  VME
     KERMIT  some assistance. The most common case will arise when one byte
     is transmitted by one system but does not arrive at the other.  KERMIT
     breaks  data up into small chunks called "packets", and if the missing
     byte is one of the ones that the KERMIT systems use to  control  these
     packets,  you  may  end  up with a machine that is waiting forever for
     something that will never arrive.
 
        The simplest way out of this possible problem is for you to keep an
     eye on the progress of the transfer and see when it appears  to  grind
     to a halt. Your micro KERMIT may display a continuous count of packets
     as  they  are  transmitted  and  received:  normally  the  number will
     increment steadily. If the number does not change  for  a  significant
     time  (and  here  you  must  bear  in  mind that the VME system may be
     running very slowly, so allow a good interval  to  pass),  your  micro
     KERMIT  may  have  a  facility,  where  you  can  manually force it to
     to  drop whatever it was doing, and retransmit its last packet of data
     to the other end. If the VME system was stuck waiting  for  data  that
     had   been  lost,  the  retransmission will prod it into life, and the
     automatic recovery mechanisms of KERMIT should allow the two  ends  to
     pick up the transfer from where it stopped.
 
        If  you wish, you can automate this recovery by using the "timeout"
     facility of VME KERMIT. This is described  below  in  the  section  on
     "Advanced facilities".
 
 
 
 
 
 
 
                                      4-5
                             VME KERMIT User Guide
 
     4.6 ADVANCED FACILITIES
     -----------------------
 
        VME  KERMIT  permits  you  to  use some more advanced techniques to
     control file transfers. Some of these  facilities  involve  the  micro
     KERMIT  system,  and  it  is possible that you will find a system that
     does not implement them, since they are fairly recent additions to the
     KERMIT specification. However, VME KERMIT will be able to detect this,
     and will act accordingly.
 
     4.6.1. Incomplete file transfers
 
          If  you  interrupt  the  reception of a file into VME KERMIT (or,
          indeed if an error such as "file full" occurs), you will be  left
          with  a  file  on  disc  that contains only part of the data that
          should have been sent. By default, VME KERMIT  will  delete  this
          partial  file  for you. If, though, you want to preserve whatever
          data has been transferred, you can issue the command
 
                              SET FILE INCOMPLETE KEEP
 
          after which VME KERMIT will close the file normally and  preserve
          it.  You can re-instate the normal situation at any time with the
          command
 
                             SET FILE INCOMPLETE DISCARD
 
     4.6.2. Using timeouts
 
          As we saw above, it is possible to automate  the  detection  that
          the  transfer  has  stopped.  This  is  done by defining "timeout
          periods": if one or other system has not received any  data  when
          its timeout expires, it will try to re-establish contact with the
          other.
 
          You  control  the  use  of  timeouts  in  two ways. The first way
          enables you to tell the micro  system what  timeout  interval  it
          should  use when receiving data from VME KERMIT. This information
          is transmitted to the micro system when  a  transfer  starts.  By
          default,  VME  KERMIT asks the micro system not to use a timeout,
          but you can change this with the SET SEND TIMEOUT command.  Note,
          though,  that  the micro system may or may not do as it is asked:
          it may not support the timeout facility; it may ignore the  value
          sent  and  use its own interval; or the timeout facility may need
          to be switched on by your giving it a command.
 
          VME  KERMIT  can  also  timeout  if data does not arrive from the
          micro  system within a given  interval.  By  default,  a  timeout
          interval of 0 seconds is set, so VME KERMIT  will never time out.
          Issuing the command
 
                                  SET RECEIVE TIMEOUT 30
 
          will set the timeout interval to 30 seconds, and VME KERMIT  will
          time  out  if  it  has  not  received any data in 30 seconds. The
          SET RECEIVE TIMEOUT command lets  you  change  this  interval  as
          required.  You can turn the timeout facility off at any time with
 
 
                                      4-6
                             VME KERMIT User Guide
 
                                 SET RECEIVE TIMEOUT 0
 
          Note  that  here  the  micro   system may ask VME KERMIT to use a
          specified timeout period when a transfer starts.
 
     4.6.3. Protocol control
 
          The rules by which files are transferred between  KERMIT  systems
          are  termed  the  "KERMIT protocol". These rules define in detail
          how data should be transferred: they specify how much can be sent
          in one chunk or packet; what control sequences indicate the start
          and end of a packet; what character encoding is to be  used,  and
          so  on.  In almost every case you will have no need to change any
          of these settings, since they are carefully chosen  so  that  any
          KERMIT  can  communicate  to any other KERMIT in just about every
          circumstance.
 
          However, it is possible that you may come across cases where  you
          need to change some of the protocol values, either to improve the
          performance of  the  file  transfer  mechanism,  or  because  the
          standard settings are inappropriate and do not work.
 
          The  protocol  values  are  changed  by  the SET command, and VME
          KERMIT  allows  you  to  change  all  the  possible  values.  The
          reference  section  details  all  the  SET commands concerned and
          their effects. A detailed discussion of the various possibilities
          is beyond the scope  of  this  user  guide,  though,  since  some
          understanding  of  the  KERMIT  protocol is needed. You will find
          this protocol explained in  the  "KERMIT  Protocol  Manual"  (use
          issue  5  or  later);  or  you  might contact the systems support
          personnel at your computer centre.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      4-7
                             VME KERMIT User Guide
 
 
 
     5: COMMANDS FOR GENERAL CONTROL OF KERMIT
     =========================================
 
        In this section, we shall look at the commands you can you can  use
     to control the general operation of VME KERMIT.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      5-1
                             VME KERMIT User Guide
 
 
 
     EXIT
 
          This  command causes VME KERMIT to return to the VME command mode
          at the end of a session.
 
          The command format is:
 
                                      EXIT
 
          There are no parameters.
 
 
          Example:
 
                                      EXIT
 
 
 
     HELP
 
          This  command  gives  information  for  the specified command, or
          allows information for a number of commands to be  requested  via
          a menu.
 
          The command format is:
 
                                  HELP <command>
 
          The parameters are:
 
          <command>
                    This parameter must be one of the VME KERMIT commands.
 
          If  the  parameter  is  omitted,  the  help  command menu will be
          displayed and you will be able to select th e command  for  which
          you require the information.
 
 
          Example:
 
                              HELP SET FILE TYPE
 
          will display the help text for the command SET FILE TYPE.
 
 
 
     SET DEBUG
 
          This command allows you turn the VME KERMIT debugging facility on
          or off.
 
          The command format is:
 
                             SET DEBUG <level> <action>
 
 
 
                                      5-2
                             VME KERMIT User Guide
 
          The parameters are:
 
          <level>
                    This  parameter  must  be one of: FILE (contents of all
                    file  records  read  or  written),  PROTOCOL  (protocol
                    states  and  events),  PACKETS (contents of all packets
                    sent or received), DEVICE (all  data  transmitted  over
                    the communications line) or ALL (all the above).
 
          <action>
                    This must be either ON or OFF.
 
          If debugging is on, VME KERMIT will output information during all
          file  transfers  to  enable  you  to  trace  errors.  It  may  be
          configured to record the protocol state, the contents of the file
          sent or received,  the  contents  of  all  packets  received  and
          transmitted, plus all the data transmitted over the communication
          line. All this information is output to the users job journal.
 
          By default, all debugging is OFF.
 
 
          Example:
 
                                SET DEBUG PACKET ON
 
          will turn on packet level debugging.
 
 
 
     SHOW
 
          This  command  displays  the  values  of  all  the KERMIT control
          values.
 
          The command format is:
 
                                      SHOW
 
          There are no parameters.
 
 
          Example:
 
                                      SHOW
 
 
 
     STATISTICS
 
          This  command  displays the statistics about the most recent file
          transfer, such as the number of packets received etc.
 
          The command format is:
 
                                   STATISTICS
 
          There are no parameters.
 
                                      5-3
                             VME KERMIT User Guide
 
          Example:
 
                                   STATISTICS
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      5-4
                             VME KERMIT User Guide
 
 
 
     6: COMMANDS FOR FILE TRANSFER
     =============================
 
        In this section we  shall  look  at  the  detailed  format  of  the
     commands  that  you  use  to  transfer  files using VME KERMIT, and to
     control how VME KERMIT will perform the transfers.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      6-1
                             VME KERMIT User Guide
 
 
 
     RECEIVE
 
          This  command causes VME KERMIT to wait for a file transfer to be
          started by the micro system. You will thus need to issue  a  SEND
          command to the micro KERMIT in order to make somethong happen.
 
          The command format is:
 
                              RECEIVE <VME-file>
 
          The parameters are:
 
          <VME-file>
                    This parameter is optional, and specifies the name of a
                    file on the VME system into which you wish data  to  be
                    transferred.
 
          When the command is issued, VME KERMIT will wait passively for  a
          signal  from the micro  KERMIT that a file transfer is beginning.
          This signal will include the name of the file that is being sent:
          if  you  have included the <VME-file> parameter, this name is for
          information only, and the data will be written to  the  file  you
          have identified.
 
          If  you omit the <VME-file> parameter, VME KERMIT will by default
          attempt to  generate  a  suitable  VME  filename  from  the  name
          supplied by the micro system.
 
 
          Example:
 
                                 RECEIVE MYFILE
 
          will  cause  VME  KERMIT  to receive a file, and to store it in a
          file called MYFILE.
 
 
 
     SEND
 
          This command sends a file to the micro KERMIT.
 
          The command format is:
 
                        SEND <VME-file> <remote-file>
 
          The parameters are:
 
          <VME-file>
                    This  parameter  is mandatory. It specifies the name of
                    the file on the VME system that you wish to  send,  and
                    can be any legal VME filename.
 
          <remote-file>
                    This  parameter  is optional. It specifies the filename
                    that VME KERMIT  will  send  to  the  micro  system  to
 
                                      6-2
                             VME KERMIT User Guide
 
                    identify the file: this may be used by the micro system
                    as the name of the file that it puts the data into, but
                    this  is  entirely  up  to  the  micro  system.  If the
                    filename is legal for the micro system, the file  would
                    normally be called by this name.
 
          You  must  issue a RECEIVE command to the micro system to prepare
          it for this SEND. You must issue the SEND first  and  then  issue
          the  RECEIVE  to  the  other  system. To allow you to do this VME
          KERMIT will pause after you issue the SEND command (by default 30
          seconds)  before  it actually starts sending. You can change this
          pause interval with the SET DELAY command.
 
          If  you  omit  the  <remote-file>   parameter, VME KERMIT will by
          default  generate  a  "generally  acceptable"   name   from   the
          <VME-file>   parameter.   It  does  this  by  stripping  off  any
          user-name, library-name, generation number etc.
 
 
          Example:
 
                                    SEND MYFILE YOURFILE
 
          causes  VME  KERMIT  to send the file MYFILE to the micro KERMIT.
          The file will be identified as YOURFILE by the micro system.
 
 
 
     SERVER
 
          This  command causes VME KERMIT to enter server mode and to wait
          for commands or file transfer requests from  the  micro  system.
          You  will  thus  be able to control the KERMIT session from your
          micro.
 
          The command format is:
 
                                   SERVER
 
          When  the  command  is issued, VME KERMIT will wait passively for
          commands and file transfer requests from the micro KERMIT.
 
 
          Example:
 
                                    SERVER
 
 
 
     SET DELAY
 
          This command sets the period for which VME KERMIT will wait after
          you issue a SEND command.
 
          The command format is:
 
                               SET DELAY <number>
 
 
                                      6-3
                             VME KERMIT User Guide
 
          The parameters are:
 
          <number>
                    The delay in seconds, in the range 5 to 300.
 
          When you issue a SEND command, VME KERMIT will do nothing for the
          specified period to enable you  to  issue  commands  to  a  micro
          system.
 
          By default, VME KERMIT will delay for 30 seconds after you  issue
          a SEND command.
 
 
          Example:
 
                                   SET DELAY 10
 
          causes  VME  KERMIT to wait for 10 seconds after receiving a SEND
          command, before starting the file transfer.
 
 
 
     SET FILE INCOMPLETE
 
          This  command  defines  what  VME  KERMIT  will  do if wither you
          interrupt the reception of a file, or if an error occurs while  a
          file is being received.
 
          The command format is:
 
                            SET FILE INCOMPLETE <action>
 
          The parameters are:
 
          <action>
                    This must be either KEEP or DISCARD.
 
          If  the action is set to DISCARD, VME KERMIT will delete any file
          whose reception is interrupted and is  thus  incomplete.  If  the
          action  is  set to KEEP, VME KERMIT will close the file normally,
          and you will be able to use whatever data was received before the
          interruption or error.
 
          By default, VME KERMIT will DISCARD an incomplete file.
 
 
          Example:
 
                         SET FILE INCOMPLETE KEEP
 
          causes VME KERMIT to save incomplete files.
 
 
 
     SET FILE NAMING
 
          This  command  defines how VME KERMIT interprets file names, when
          the VME filename  or  the  remote  filename  are  not  explicitly
          stated.
                                      6-4
                             VME KERMIT User Guide
 
          The command format is:
 
                            SET FILE NAMING <action>
 
          The parameters are:
 
          <action>
                    This must be either NORMAL-FORM or UNTRANSLATED.
 
          If  the  action  is  set  to  NORMAL-FORM,  VME KERMIT will, when
          sending a file, and the remote filename is  omitted,  attempt  to
          genrate  a  "generally acceptable" name from the VME filename. It
          does  this  by  stripping  off   any   user-name,   library-name,
          generation  number etc. Similarly, when receiving a file, and the
          VME filename is omitted, VME KERMIT will attempt  to  generate  a
          suitable name from the name supplied by the remote KERMIT.
 
          If  action  is  set  to UNTRANSLATED, VME KERMIT will not attempt
          to generate a standardised name.
 
          By default, VME KERMIT will normalise filenames.
 
 
          Example:
 
                         SET FILE NAMING UNTRANSLATED
 
          will turn off file normalisation.
 
 
 
     SET FILE OVERWRITE
 
          This command specifies the action that VME KERMIT  must  take  on
          reciving  a  file  if  the  name it tries to store the data under
          clashes with an existing file.
 
          The command format is:
 
                           SET FILE OVERWRITE <action>
 
          The parameters are:
 
          <action>
                    This must be either ON or OFF.
 
          If  the  file  overwrite  facility  is  ON, VME KERMIT will check
          whether the name it wishes to use to store incoming data  clashes
          with an existing file name. If it does, VME KERMIT will overwrite
          the file with the new data.
 
          If file overwrite is OFF, VME KERMIT will not overwrite the file,
          but will report an error.
 
          By default, file overwrite is OFF.
 
 
 
 
                                      6-5
                             VME KERMIT User Guide
 
          Example:
 
                              SET FILE OVERWRITE ON
 
          turns on the file overwrite facility.
 
 
 
     SET FILE TYPE EBCDIC
 
          This  command  tells  VME  KERMIT  that  files  it  transmits and
          receives  are  to  taken  as  containing  printable text  and  to
          transform them accordingly.
 
          The command format is:
 
                       SET FILE TYPE EBCDIC
 
          There no parameters.
 
          After  using  this  command,  VME  KERMIT  treats  all  files  as
          containing printable text. When sending a file, it will translate
          all EBCDIC text to ASCII, and transform every end of record  into
          KERMIT's  standard "end of line" terminator, and the micro KERMIT
          should then change this into whatever the standard representation
          of  end-of-line  is  on its own system. When receiving files, VME
          KERMIT will translate all ASCII text to EBCDIC, and  treat  every
          occurrence  of  the  standard KERMIT "end-of-line" indicator as a
          record terminator.
 
          Note,  you  may  need  to give an equivalent command to the micro
          KERMIT system to make it treat the data correctly.
 
          By  default, VME KERMIT treats files as EBCDIC.
 
 
          Example:
 
                              SET FILE TYPE EBCDIC
 
          makes VME KERMIT treat files as containing EBCDIC data.
 
 
 
     SET FILE TYPE ASCII
 
          This  command  tells  VME  KERMIT  that  files  it  transmits and
          receives are to taken as containing ASCII text and  to  transform
          them accordingly.
 
          The command format is
 
                       SET FILE TYPE ASCII
 
          There no parameters.
 
          After using this command, VME KERMIT will transmit the characters
          from  the  file  exactly  as they are, and will not change any of
 
                                      6-6
                             VME KERMIT User Guide
 
          them. Similary the data it receives will be written to file  with
          no  alteration.  However,  as  with EBCDIC files, VME KERMIT will
          maintain the record format.
 
          Note,  You  may  need  to give an equivalent command to the micro
          KERMIT system to make it treat the data correctly.
 
          By default, VME KERMIT treats files as EBCDIC.
 
 
          Example:
 
                              SET FILE TYPE ASCII
 
          makes VME KERMIT treat files as containing ASCII data.
 
 
 
     SET FILE TYPE BINARY
 
          This command tells VME KERMIT that all files it receives or sends
          should be treated as containing binary data.
 
          The command format is:
 
                              SET FILE TYPE BINARY
 
          There are no parameters.
 
          After using this command, VME KERMIT will transmit the bytes from
          a file exactly as they are, and will  not  change  any  of  them.
          Similarly,  the  data it receives will be written to file with no
          alteration.
 
          Note,  You  may  need  to give an equivalent command to the micro
          KERMIT system to make it treat the data correctly.
 
          By default, VME KERMIT treats files as EBCDIC.
 
 
          Example:
 
                              SET FILE TYPE BINARY
 
          makes VME KERMIT treat files as containing binary data.
 
 
 
     SET RECEIVE TIMEOUT
 
          This  command  defines  the  interval after which VME KERMIT will
          take action if it has received no data from the micro system.
 
          The command format is:
 
                         SET RECEIVE TIMEOUT <interval>
 
 
 
                                      6-7
                             VME KERMIT User Guide
 
          The parameters are:
 
          <interval>
                    Specifies the timeout period in seconds, in the range 0
                    to 94.
 
          The command defines the timeout that VME KERMIT is to use.
          The  choice  of  the  timeout period will depend on many factors.
          Regard should be paid to how fast the VME system is operating, it
          could  be  running slowly due to heavy use and also to the delays
          that  operating  over a network may  impose. Care should be taken
          not to set the value too  low,  or  VME  KERMIT  will  repeatedly
          timeout unnecessarily.
 
          By default, a timeout interval of 0 seconds is set.
 
 
          Example:
 
                             SET RECEIVE TIMEOUT 10
 
          causes  VME  KERMIT to timeout if no data has been received after
          10 seconds.
 
 
 
     SET SEND TIMEOUT
 
          This command sets the timeout interval that VME KERMIT  asks  the
          micro  system to use. The micro  system should timeout if no data
          has been received from VME KERMIT after this interval.
 
          The command format is:
 
                          SET SEND TIMEOUT <interval>
 
          The parameters are:
 
          <interval>
                    specifies  the  interval  required  in  seconds, in the
                    range 0 to 94.
 
          VME KERMIT will pass this value  to  the  micro   system  at  the
          beginning  of  every  file  transfer.  Note,  though,  that it is
          entirely up to the micro  system  whether  it  uses  this  value,
          ignores  it, or uses a value of its own. You may need to give the
          micro  system commands to turn its timeout facility on.
 
          By default, VME KERMIT requests the micro system to set a timeout
          value of 0 seconds.
 
 
          Example:
 
                              SET SEND TIMEOUT 10
 
          causes  VME  KERMIT  to ask the micro  system to timeout after 10
          seconds if no data has been received from the VME system.
 
                                      6-8
                             VME KERMIT User Guide
 
 
     7: COMMANDS FOR DETAILED PROTOCOL CONTROL
     =========================================
 
        The commands described in this section are used to  exert  detailed
     control over the KERMIT protocol. As explained earlier, it is unlikely
     that you would ever need to use these commands. You should consult the
     KERMIT  Protocol  Manual  for a detailed description of the facilities
     they control.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      7-1
                             VME KERMIT User Guide
 
 
 
     SET PAUSE
 
          This command defines a "turn-round" delay that  VME  KERMIT  will
          use  in  packet transmission. It defines the time that VME KERMIT
          will wait, after receiving  a  packet  from  the  micro   system,
          before  transmitting the next to it. This overcomes problems with
          some systems that cannot accept input that comes too  soon  after
          output.
 
          The command format is:
 
                               SET PAUSE <number>
 
          The parameters are:
 
          <number>
                    The pause time in tenths of a second, in the range 0 to
                    50.
 
          By  default, VME  KERMIT does not pause (i.e. the pause value is
          0).
 
 
          Example:
 
                                  SET PAUSE 1
 
          causes VME KERMIT  to  pause  for  1  tenth  of  a  second  after
          receiving one packet before sending the next.
 
 
 
     SET RECEIVE END-OF-LINE
 
          This  command defines the value that VME KERMIT request the other
          end to use to signal the end of a packet.
 
          The command format is:
 
                        SET RECEIVE END-OF-LINE <number>
 
          The parameters are:
 
          <number>
                    The number of the control character in the range  0  to
                    31 or 127. Note, a number of the control characters are
                    not accepted by VME as a valid  end-of-line  terminator
                    (see Appendix 2).
 
          By  default,  VME  KERMIT  asks for packets to be terminated with
          Carriage Return (hex 0D).
 
 
 
 
 
 
                                      7-2
                             VME KERMIT User Guide
 
          Example:
 
                          SET RECEIVE END-OF-LINE X09
 
          requests the micro KERMIT to terminate  packets  with  Horizontal
          Tab (code hex 09).
 
 
 
     SET RECEIVE PACKET-LENGTH
 
          This command defines the maximum packet size that VME KERMIT will
          ask the micro  system to send.
 
          The command format is:
 
                       SET RECEIVE PACKET-LENGTH <number>
 
          The parameters are:
 
          <number>
                    The  maximum  size  of  packet  wanted  from the micro
                    system, in the range 30 to 94.
 
          By default, VME KERMIT asks the micro  system to  use  a  maximum
          packet size of 80 bytes.
 
 
          Example:
 
                          SET RECEIVE PACKET-LENGTH 60
 
          causes  VME  KERMIT to request the micro  system to use a maximum
          packet size of 60 bytes.
 
 
 
     SET RECEIVE PAD-CHARACTER
 
          This  command  defines  the  control  character  that  VME KERMIT
          requests the other to use when padding before sending a packet.
 
          The command format is:
 
                       SET RECEIVE PAD-CHARACTER <number>
 
          The parameters are:
 
          <number>
                    The  numeric  code  of the control character to be used
                    for padding in the range 0 to 31 or 127. Note, a number
                    of  the  control  characters are not accepted by VME as
                    valid pad characters (see Appendix 2).
 
          By default, VME KERMIT will ask for a pad character of code 0.
 
 
 
 
                                      7-3
                             VME KERMIT User Guide
 
          Example:
 
                          SET RECEIVE PAD-CHARACTER X00
 
          requests the micro  KERMIT to pad with NUL characters (code 0).
 
 
 
     SET RECEIVE PADDING
 
          This command defines the number of pad characters that VME KERMIT
          will ask the other end to send before each packet.
 
          The command format is:
 
                          SET RECEIVE PADDING <number>
 
          The parameters are:
 
          <number>
                    The number of pad characters to be  requested,  in  the
                    range 0 to 94.
 
          By default, VME KERMIT asks for no pad characters to be sent.
 
 
          Example:
 
                             SET RECEIVE PADDING 10
 
          will  cause  VME  KERMIT  to request the micro  system to precede
          each packet with 10 pad characters.
 
 
 
     SET RECEIVE START-OF-PACKET
 
          This  command  defines  to VME KERMIT the control character that
          the micro system will use to indicate the start of each packet.
 
          The command format is:
 
                      SET RECEIVE START-OF-PACKET <number>
 
          The parameters are:
 
          <number>
                    The  numeric  code  of  the character the micro  system
                    will use, in the range 0 to 31 or 127. Note,  a  number
                    of  the  control  characters are not accepted by VME as
                    a valid start-of-packet marker (see Appendix 2).
 
          By default, VME KERMIT will expect the micro  system  to  precede
          each packet with a hex 1E character.
 
 
 
 
 
                                      7-4
                             VME KERMIT User Guide
 
          Example:
 
                        SET RECEIVE START-OF-PACKET X07
 
          tells  VME KERMIT that the micro  system will precede each packet
          with a hex 07 character.
 
 
 
     SET RETRY
 
          This  command  sets  the maximum number of times that VME KERMIT
          will attempt to send or receive a packet before  abandoning  the
          transfer.
 
          The command format is:
 
                      SET RETRY <number>
 
          The parameters are:
 
          <number>
                    The  maximum  number of retries to be attempted, in the
                    range 0 to 10.
 
          By default, VME KERMIT will retry transfers 4 times.
 
 
          Example:
 
                        SET RETRY 7
 
          sets the packet retry limit to 7.
 
 
 
     SET SEND EIGTH-BIT-PREFIX
 
          This command defines  the  eigth-bit-prefix  character  that  VME
          KERMIT will ask the micro system to agree to use.
 
          The command format is:
 
                        SET SEND EIGTH-BIT-PREFIX <character>
 
          The parameters are:
 
          <character>
                    The printable character to be used.
 
          By  default,  VME KERMIT will attempt to use the "&" character as
          its eigth-bit prefix.
 
 
 
 
 
 
 
                                      7-5
                             VME KERMIT User Guide
 
          Example:
 
                             SET SEND EIGHT-BIT-PREFIX %
 
          sets the eigth-bit prefix character to be "%".
 
 
 
     SET SEND END-OF-LINE
 
          This  command  defines the control character that VME KERMIT will
          use to terminate the first packet it sends to the micro system in
          each  transfer.  Subsequent  packets  will  be  terminated by the
          character that the micro system requests in its SEND-INIT packet.
 
          The command format is:
 
                         SET SEND END-OF-LINE <number>
 
          The parameters are:
 
          <number>
                    The  numeric  code  of the character to be used, in the
                    range 0 to 31 or 127. Note, a  number  of  the  control
                    characters   are   not  accepted  by  VME  as  a  valid
                    end-of-line terminator (see Appendix 2).
 
          By default, VME KERMIT uses hex 0D (Carriage Return).
 
 
          Example:
 
                            SET SEND END-OF-LINE 9
 
          causes the first packet sent in each transfer to  be  ended  with
          Horizontal Tab (code 9).
 
 
 
     SET SEND PAD-CHARACTER
 
          This  command defines the padding character with which VME KERMIT
          will  precede  the  first  packet  to  be  sent  in  a  transfer.
          Subsequent packets will be preceded by the character requested by
          the micro  system in its SEND-INIT packet.
 
          The command format is:
 
                           SET SEND PADCHAR <number>
 
          The parameters are:
 
          <number>
                    The  numeric  code  of the character to be used, in the
                    range 0 to 31 or 127. Note, a  number  of  the  control
                    characters  are  not  accepted  by  VME  as a valid pad
                    character (see Appendix 2).
 
 
                                      7-6
                             VME KERMIT User Guide
 
          By default, VME KERMIT uses a pad character of NUL (code hex 0).
 
 
          Example:
 
                              SET SEND PADCHAR X1A
 
          sets the pad character used to be hex 1A.
 
 
 
     SET SEND PADDING
 
          This command defines the number of pad characters VME KERMIT will
          send before the first packet in a  transfer.  Subsequent  packets
          will  be preceded by the number requested by the micro  system in
          its SEND-INIT packet.
 
          The command format is:
 
                           SET SEND PADDING <number>
 
          The parameters are:
 
          <number>
                    The number of pad characters to be sent, in the range 0
                    to 94.
 
          By default, VME KERMIT sends no pad characters.
 
 
          Example:
 
                              SET SEND PADDING 21
 
          causes VME KERMIT to send 21  pad  characters  before  its  first
          packet.
 
 
 
     SET SEND QUOTE
 
          This  command  defines  the character that VME KERMIT will use to
          prefix control characters in data packets that it sends.
 
          The command format is:
 
                           SET SEND QUOTE <character>
 
          The parameters are:
 
          <character>
                    The printable character to be used.
 
          By  default,  VME KERMIT uses the "#" character (hash). Note that
          the "hash" character appears as "pound"  on  some  keyboards  and
          printers.
 
 
                                      7-7
                             VME KERMIT User Guide
 
          Example:
 
                                SET SEND QUOTE $
 
          causes VME KERMIT to prefix control characters it sends  in  data
          packets with a "$".
 
 
 
     SET SEND START-OF-PACKET
 
          This  command  defines the control character that VME KERMIT will
          send to indicate the start of every packet.
 
          The command format is:
 
                       SET SEND START-OF-PACKET <number>
 
          The parameters are:
 
          <number>
                    The numeric code of the character to be  sent,  in  the
                    range  0  to  31  or 127. Note, a number of the control
                    characters  are  not  accepted  by  VME  as   a   valid
                    start-of-packet marker (see Appendix 2).
 
          By default, VME KERMIT sends a hex 1E character in front of every
          packet.
 
 
          Example:
 
                               SET SEND START-OF-PACKET X08
 
          causes  VME KERMIT to precede every packet it sends with a hex 08
          character.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      7-8
                             VME KERMIT User Guide
 
 
     8: OBTAINING, BUILDING AND MODIFYING VME KERMIT
     ===============================================
 
        This chapter describes how you can get hold of VME KERMIT and build
     it  from  the  S3  and  MTUP  language  sources, or modify an existing
     version.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      8-1
                             VME KERMIT User Guide
 
 
     8.1 OBTAINING VME KERMIT
     ------------------------
 
        You can obtain the VME KERMIT files by file transfer over the JANET
     or  PSS   networks,   or  by  using  KERMIT  itself,  from   Lancaster
     University.
 
     You  will eventually have a set of S3 and MTUP source files from which
     you  need  to  generate compiled OMF. There are two SCL files: KERMIT,
     an interface procedure, and KMT_SCL which is executed to  compile  and
     collect your version of VME KERMIT.
 
 
     8.1.1 The source files
 
          VME  KERMIT  source  is held in a fair number of files and is now
          quite  large  (and  still  growing).  The  source  is  split   by
          functionality.  The organisation is not fixed, we shall refine it
          with experience and as the system changes, so the names  are  not
          guaranteed to be unchanged from one release to another.
 
          For version 1.01 and later, the files that make up VME KERMIT are
          are as follows:
 
          VME  KERMIT  as  issued consists of four types of file. The first
          type consists of the S3 source files:
 
               KMT_DATA_MODULE        Global declarations.
               KMT_DH_MODULE          Communications device handling code.
               KMT_EH_MODULE          Error handling code.
               KMT_FH_MODULE          File handling code.
               KMT_MAIN_MODULE        Entry code.
               KMT_PH_MODULE          Protocol handling code.
               KMT_PP_MODULE          Packet handling code.
               KMT_SP_MODULE          Support procedures.
               KMT_UI_MODULE          User interface code.
 
           The second type of the file consists of the MTUP source files:
 
               KMT_HELP_MTM           Help message texts.
               KMT_SP_MTM             Support procedures message texts.
 
           The  third  type of file consists of SCL files.
 
               KERMIT                 Interface procedure.
               KMT_SCL                Compilation and collection SCL.
 
           The fourth type of file consists of the User Guide:
 
               VME_KMIT_DOC           User Guide documentation.
 
 
 
 
 
 
 
 
                                      8-2
                             VME KERMIT User Guide
 
 
     8.3 BUILDING VME KERMIT FROM SOURCE
     -----------------------------------
 
        Prior  to  generating  VME  KERMIT  check  that  the SCL interface
     procedure KERMIT meets your requirements. In particular,  ensure  that
     the  BOOL  value  ASG  is  set appropriately. It should be set TRUE if
     terminal connection to VME is via ASG, but FALSE  if  via  some  other
     communications  controller,  eg NIC or CSC. If in doubt set ASG FALSE.
     The purpose of this BOOL is to allow  checking  of  control  character
     setting  for  START-OF-PACKET  etc.  VME I/O is not transparent to all
     control characters. The ASG can handle a superset  of  the  characters
     that can be handled by CSC or NIC.
 
        If you wish to change the default VME KERMIT option (see 3.1)  this
     can be altered most easily in the SCL interface procedure KERMIT.
 
        Generating VME KERMIT from the S3 and MTUP sources is a fairly easy
     process.  Having  transferred  the files to your VME filestore you can
     compile them by executing the SCL file KMT_SCL. Edit this file to suit
     your VME filestore, then execute the SCL file as follows:
 
                               EXSCL(FIL=KMTSRC.KMTSCL)
 
 
 
     8.4 CHANGING KERMIT DEFAULTS
     ----------------------------
 
       If you have the S3 compiler, you can change the defaults by altering
     the  values  held  in  the  source  files (in particular the procedure
     KMT_SP_SET_DEFAULTS in KMT_SP_MODULE) and re-compiling the source.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                      8-3
                             VME KERMIT User Guide
 
 
 
     Appendix 1. VME KERMIT capabilities
     ===================================
 
        Local operation:                 No
        Remote operation:                Yes
        Transfer text files:             Yes
        Transfer binary files:           Yes (prefix only)
        Wildcard send:                   No
        ^X/^X interruption:              Yes (receive only)
        Filename collision avoidance:    Yes
        Can timeout:                     Yes
        8th-bit prefixing:               Yes
        Repeat count prefixing:          No
        Alternate block checks:          No
        Terminal emulation:              No
        Communications settings:         No
        Transmit BREAK:                  No
        IBM communication:               No
        Diagnostic logging:              Yes
        Session logging:                 No
        Raw transmit:                    No
        Act as server:                   Yes
        Talk to server:                  No
        Advanced server commands:        No
        Local file management:           No
        Handle file attributes:          No
        Command/init files:              No
        Host commands:                   No
        Printer control:                 No
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                     A1-1
                             VME KERMIT User Guide
 
 
 
     Appendix 2. Valid VME control characters
     ========================================
 
        The control characters that are acceptable to VME depend on the
     communications device through which the terminal running Kermit is
     routed. The ASG permits a greater range of control characters than
     do CSC or NIC.
 
 
          Character              Input via               Output via
     name   dec   hex          ASG     CSC/NIC          ASG     CSC/NIC
 
      NUL    0     00           +         -              +         +
      SOH    1     01           +         -              -         -
      STX    2     02           +         -              +         +
      ETX    3     03           +         -              -         -
      EOT    4     04           +         -              -         -
      ENQ    5     05           +         -              +         +
      ACK    6     06           +         -              +         +
      BEL    7     07           +         +              +         +
 
      BS     8     08           +         +              +         +
      HT     9     09           +         -              +         +
      LF    10     0A           +         -              -         -
      VT    11     0B           +         -              +         +
      FF    12     0C           +         -              +         +
      CR    13     0D           +         -              +         +
      SO    14     0E           +         +              +         +
      SI    15     0F           +         +              +         +
 
      DLE   16     10           -         -              +         +
      DC1   17     11           -         -              +         +
      DC2   18     12           -         -              +         +
      DC3   19     13           -         -              +         +
      DC4   20     14           +         +              +         +
      NAK   21     15           +         -              +         +
      SYN   22     16           +         -              +         +
      ETB   23     17           +         -              +         +
 
      CAN   24     18           +         -              +         +
      EM    25     19           +         +              +         +
      SUB   26     1A           +         +              +         +
      ESC   27     1B           +         +              +         +
      FS    28     1C           +         +              +         +
      GS    29     1D           +         +              +         +
      RS    30     1E           +         +              +         +
      US    31     1F           +         +              +         +
 
      DEL  127     7F           +         +              +         +
 
 
 
 
 
 
 
 
                                     A2-1
                             VME KERMIT User Guide
 
 
 
     Appendix 3. Running KERMIT over a JNT PAD
     =========================================
 
        KERMIT  may  be  ran  over a JNT PAD, but special attention must be
     made to the KERMIT configuration parameter settings  and  to  the  PAD
     settings.  The  choice of the KERMIT start of packet marker and end of
     line terminator will dictate the PAD settings required. Normally,  the
     additional  PAD  settings  of  TRANSPARENT  and  NOPRINTMASK  will  be
     sufficient. However, the FORWARD and LFINSERT PAD  settings  may  also
     require consideration.
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
 
                                     A3-1
                             VME KERMIT Questionaire
 
 
 
     Please reply to the following questions and return to:
 
                      David Lord,
                      S.W.U.R.C.C.
                      The University Of Bath,
                      Claverton Down,
                      Bath.
                      BA2 7AY.
 
 
     1. Name of organisation:
 
 
 
     2. Address of organisation:
 
 
 
 
 
 
 
 
     3. Specify  the  KERMIT  implementations  with which VME KERMIT is to
        operate.
 
 
 
 
 
 
 
 
 
 
 
 
     4. List  any  problems  encountered  during  the  installation of VME
        KERMIT.
 
 
 
 
 
 
 
 
 
 
 
 
     5. Comment on the contents and structure of the User Guide.
 
 
 
 
 
 
                             VME KERMIT Questionaire
 
 
 
 
 
 
 
     6. Other comments.